## Slide 1
An Overview of PIM Configurations
Flavors Technology
Notes: 1
The following presentation provides an overview of the various PIM configurations since 1990. Though some are no longer offered, they are included in this presentation to provide the reader with an overview of the product evolution.
Through each implementation of the PIM, Paracell, and the Paracell Navigator have remained the language and development environment respectively. Over the years, the software has also been enhanced to provide a rich development environment and an easy to use, productive language.

## Slide 2
“Fridge” PIM
BusLink™
• Up to 16,384 Cells
• 60Hz FIXED frame rate
• Real-time
• Expensive!
- to start
- to expand
• No longer sold
Notes: 2
The first PIM developed and deployed was the “Fridge” PIM. This unit was based on a proprietary configuration of standard components. The PIM was developed from the start to be a platform for deployed, mission-critical applications. Each of the four types of PC boards, the Boss (system control), Multiprocessor (MP), I/O board, and Global Memory (GM) were mounted on anodized plates with a patented thermal rubber pad. A Fridge PIM system could be configured with a minimum 512 processing cells, all the way up to 16,384 processing cells. Boards were held in a stainless steel, shielded enclosure that featured active cooling, 208V/3 phase DC power, and separate battery backup.
This early PIM ran at a fixed 60Hz frame rate. Sixty times a second, all processing cells would read from global memory, execute their code, and write the results back to global memory. Communication within the Fridge PIM occurred over the PIMbus, a high-speed, isolated bus designed for communication between MP, I/O, GM, and the Boss Board.
The development environment ran on a Macintosh workstation, and was connected to the PIM via a shared memory interface known as the Bus-Link™, Flavors’ original product line. This early PIM was installed at GM Truck & Bus, and was evaluated in applications at the Electric Power Research Institute and in Japan. This product is no longer sold.

## Slide 3
“Rocket” PIM
Rocket
Card(s)
• MacBus = PIMbus
• 60Hz - 30Hz variable frame rate
• Real-time
• Multiple PIM system via TCP/IP
• 1K Cells Max
• Reliability based on status of
Macintosh NuBus
• No longer sold
Notes: 3
The “Rocket” PIM was the next version of the PIM family, so named as the PIM processing engine resided on a Radius Rocket accelerator board. The Rocket PIM boards plugged directly into the NuBus slots of a Macintosh Quadra-class workstation, thus allowing the development environment and execution engine to live on the same workstation.
This version of the PIM was the first to feature a variable frame rate, or scan time. PIM execution time could be varied in an inverse relationship with number of cells available. For example, if speed were doubled, number of available cells were halved.
Though a number of Rocket PIMs were sold and installed, this version of the product had its shortcomings. The PIM execution hardware was dependent upon the stability of the Macintosh NuBus limiting the RocketPIMs applicability in a mission-critical situation. Further, the RocketPIM had a limitation of 1000 processing cells. Though up to four boards could be placed in a Macintosh workstation, this limitation restricted scalability of the PIM.
This version of the PIM has since been phased out in favor of the latest configurations in the product line - the VME PowerPIM and the NT-PIM.

## Slide 4
PowerPIM
TCP/IP
VME-PPC
boards
• MacBus & VMEbus isolated
• 8K Cell Max
• TCP/IP via Ethernet
• Real-time
• 60/30/15Hz frame rates
• Multiple PIM system via TCP/IP
• Ideal for hard real-time, mission
critical applications
Notes: 4
The VME PowerPIM is the currently offered configuration of the PIM for applications demanding hard real-time control. In this configuration, the development and delivery platforms are on completely separate bus structures. PIM applications run on one, or a combination of multiple VME Power PC 604e boards while the development of applications in Paracell takes place on a Macintosh G3/4 or Intel-based workstation.
The PowerPIM is a scalable solution, ranging from 250 to 8000 processing cells per VME enclosure, depending upon the frame rate required by the application. Additionally, multiple VME PowerPIMs can be networked together via TCP/IP to provide a common distributed solution. For example, in the Japanese Railway PIM application, ten VME enclosures are networked to provide a real-time simulation environment.
The VME PowerPIM features I/O boards that support TCP/IP and DeviceNet™ I/O, making this platform ideal for discrete manufacturing and process control solutions that can benefit from an agent-architecture and guaranteed, predictable performance. In addition, PowerPIM can be configured with Flash Memory so that the state of the application can be stored in a single frame for quick application restarts.
Of course, applications for the PowerPIM are developed using Paracell and the Paracell Navigator environment, thus benefiting from the productivity of the language and the rich tools in the programming environment.

## Slide 5
NT-PIM (Standalone & Runtime)
TCP/IP
Or….
BOTH CONFIGURATIONS:
• “Any” frame rate
• “Any” number of cells
• “Real-time”
Runtime Platform:
• Navigator on Mac or PC
• Connect to NT-PIM via TCP/IP
Standalone Platform:
• Navigator and PIM run
on the same platform
Notes: 5
The latest addition to the PIM family of products is the NT-PIM. In this configuration, the PIM engine executes on a laptop or desktop running Windows NT 4.0. Like the PowerPIM, the NT-PIM features a variable frame rate and can be configured with up to 4,000 processing cells. The major difference between the PowerPIM and the NT-PIM lies in real-time performance. Where the PowerPIM is guaranteed real-time, the real-time performance of the NT-PIM is “soft.” That is, it can be affected by the amount of processing time NT provides to the PIM application.
An NT-PIM can be configured stand-alone, whereby the PIM and the Paracell Navigator environment are resident on the same platform, or as a runtime platform, where the development environment is connected to the NT-PIM via TCP/IP.
The NT-PIM is an ideal environment for simulations, or for development of applications that will subsequently run on a PowerPIM. Applications developed on one can be seamlessly migrated to the other. Both benefit from the power and productivity of the Paracell programming language and the Paracell Navigator development environment.
Overall, the NT-PIM offers a cost-effective way to take advantage of agent-based systems and architectures, and to implement powerful, robust simulations and solutions.

## Slide 6
System Components
1. The Paracell Navigator Environment
Paracell compiler, debug, programming
2. PIM Runtime Environment
Run cells and execute tiles
3. Human/Machine Interface
Display PIM data execution
Accepts operator input
Notes: 6
Over the history of the PIM configurations, the development environment, architecture, and HMI philosophy has remained constant.
The Paracell Navigator environment is where Paracell applications are developed. The language and the programming model were designed from the ground-up to take advantage of a parallel architecture, and to provide a way to easily develop agent-based solutions. The Navigator environment provides a 3x3 matrix that extends ten levels deep so that code can be decomposed easily. The environment also provides a rich set of tools, including debuggers, trackers, and a powerful compiler and download utility.
The PIM runtime environment is based on a read-execute-write model. Each frame, all of the processor cells read their inputs from global memory, execute their code, and simultaneously write their results back to global memory so that the information is available on the next frame. Though two processing cells may update the same variable, the Navigator provides utilities to determine which update has precedence. This “systolic” execution model plays a key part in guaranteeing each processor ample resources, which in turn provides guaranteed, predictable performance.
HMI and interaction with the PIM and data has always been a key building block of the product. Beyond the visual programming environment of the Navigator, the ParaScope utility allows PIM values to be displayed in powerful, mainstream HMI environments such as LabView by National Instruments. This interface between the PIM and COTS HMI environments is bi-directional, in that ParaScope will pass user-entered data from the LabView display to the PIM.

## Slide 7
Key Enhancements
“SoftPIM” (NT-PIM)
Variable Frame Rates
New Paracell Compiler
Floating Point
Human/Machine Interface
  SoftScope
  ParaScope
I/O via TCP/IP or DeviceNet™
Notes: 7
To quickly summarize some of the key changes in PIM software and I/O…
The NT-PIM is the first generation of the PIM that runs completely in software in a Windows NT 4.0 (Service Pack 4 or better) environment.
Frame Rates of the PIM can be varied in all currently offered configurations. This is done in an inversely proportional manner to the number of cells required. For example, a 100 cell system at 60Hz will provide 200 cells at 30Hz.
The latest version of the Paracell Compiler has been significantly updated. In addition to Floating Point capability, a number of new features and functions have been added as well. For more information about the new compiler, please visit the Product Documentation section of our website.
The original HMI environment of the PIM, SoftScope, remains available for the Macintosh version of the Paracell Navigator, however ParaScope has been introduced as a way to provide more elegant HMI solutions using mainstream, HMI specific products such as LabView. ParaScope works in both a Macintosh and a Wintel environment.
In addition to the TCP/IP I/O that has been available since the RocketPIM, Flavors now offers DeviceNet I/O. The products also support file I/O in formats such as .xls, .dbf, and so on.

## Slide 8
Mixed NT-PIM System
Mac or PC Navigator
NT-PIM
ParaScope
HMI (1 to n)
Mac or PC
TCP/IP
Notes: 8
Any of the available PIM configurations can be applied in a mix-and-match environment as dictated by the requirements of the application. On the pages that follow, some examples are provided.
In the example shown above, a Macintosh G3/G4 or an Intel Pentium-based workstation serve as the development environment. This is where the Paracell Navigator development environment resides, and where Paracell applications are developed and tested.
The development platform is connected to an NT-PIM via TCP/IP. The PIM runtime software resides on the Intel-based laptop or desktop as shown. The NT-PIM in turn connects to any number of Macintosh G3/G4 or Intel platforms providing HMIs via ParaScope and LabView. This interface is also accomplished via the TCP/IP protocol.
Note that although it is not depicted, there can be 1 - X NT-PIM platforms interconnected to serve the needs of the application.

## Slide 9
Mixed PowerPIM System
Mac or PC
Navigator
PowerPIM
(1 to n via TCP/IP)
ParaScope HMI
(1 to n via TCP/IP)
TCP/IP
Plant Floor
I/O
Notes: 9
Above, the configuration is similar, however instead of the NT-PIM hosting the PIM runtime software, we have shown a VME PowerPIM. This represents a typical configuration that might be found in an application demanding hard real-time performance, such as a control application in manufacturing or process control.
Note again that any number of VME PowerPIMs can be connected via TCP/IP as dictated by application requirements. This example also shows a connection to plant floor I/O via a Flavors I/O Processor (IOP), which provides a DeviceNet™ interface to the factory floor.
Again, HMI is accomplished through a number of Macintosh G3/G4 or Intel-based computers running ParaScope and LabView. Configurations of up to twenty PIMs interconnected via TCP/IP have been successfully implemented in this manner.

## Slide 10
Standalone System
PC Navigator
NT-PIM
ParaScope HMI
Notes: 10
For off-site development or for simulation systems, Flavors offers the standalone NT-PIM.
As shown above, the Paracell Navigator development environment, ParaScope HMI through LabView, and the PIM runtime all reside on the same Intel-based platform. As previously mentioned, the NT-PIM comes closest to real-time performance when the NT-PIM engine is the only software running on the platform. However, even in the configuration shown above where the PIM engine shares processing time with the Navigator and LabView, the PIM execution model remains constant. In other words, all cells reading, executing, and writing is maintained.
This becomes important when the standalone configuration is used for development of solutions that will subsequently be migrated to another configuration, such as a PowerPIM. By keeping the model and execution consistent, developers can expect equal or better performance of their solutions when they are migrated to a dedicated PIM engine.
In the meantime, for development of simulations or for demonstrations of how a solution might be implemented using an agent-based system, the standalone NT-PIM offers an ideal cost-effective platform.

## Slide 11
Develop & Deploy
Mac or PC
Navigator
PowerPIM
(1 to n via TCP/IP)
ParaScope HMI
(1 to n via TCP/IP)
NT-PIM/Nav/HMI
For on-going development
TCP/IP
Notes: 11
The example above is simply a mix-and-match of all available PIM platforms and functionality. All of the components described in black text are exactly the same as our previous example. The difference is that in this illustration, an NT-PIM has been added to aid ongoing development.
A copy of the Navigator database can be copied to the NT-PIM from the primary development platform. At a minimum, the NT-PIM can host the PIM engine and the Paracell Navigator for continued off-line development of an application. Obviously this NT-PIM can also host ParaScope and LabView so that additional development on HMI can occur.
The development database can subsequently be loaded into the PIM, and the changed or newly developed Paracell code copied back to the primary development environment.
As shown in this and the previous examples, the PIM family of products offers the flexibility you need to experiment with, develop, and deploy predictable, effective agent-based solutions in the shortest amount of time.

## Slide 12
PIM Pricing Model
PIM Hardware
PIM Software
Paracell and the Paracell Navigator
PIM Cells
PIM Accessories
Service, Support, Application Development and Customized Solutions
Notes: 12
PIM pricing is based on a combination of the hardware required to host the PIM and the development environment, software license fees, and tiered cell pricing. In addition, there are accessories that can be added to a configuration.
Hardware to support a PIM installation can be bought by Flavors, or we can provide you with specifications and vendor contacts so that prices and terms can be negotiated directly.
Software license fees include PIM runtime software and development environment software. Though the development environment pricing is fixed, the runtime license can vary based on configuration, such as single-board VME vs. multiple board VME vs. NT-PIM.
A “per cell” license fee exists for the processing cells. Processing cells are sold in a tiered system, whereby when an application demands more cells, the price per cell drops at several tiers. For those similar with database systems, this is similar to the approach taken by Oracle in pricing by size of the database.
PIM accessories include the Flash Memory option, ParaScope drivers, LabView HMI, and I/O.
Finally, service, support, training, and customized development of both applications and I/O sub-systems can be provided.
If you are interested in discussing an application, please give us a call so that we can work with you to determine the best platform, and to size the PIM according to your needs. This will result in a quotation that you can take under consideration.